## Slide 1
The impact of non-tidal surface loading deformation on GNSS coordinate time series
B. Männel1, S. Glaser1, A. Brandt1, and H. Schuh1,2
1 German Research Centre for Geosciences, Potsdam
2 Technische Universität Berlin

## Slide 2: Introduction
Comparison of annual & semiannual amplitude and phase
Reduction of RMS (linear trajectory model), Reduction of periodic signals
Non-tidal loading models (ESMGFZ)
ITRF2020
GFZ repro3 solution
Periodic signals vs. NTL models
Correction at solution level
Correction at observation level
Periodic function:

## Slide 3: Periodic signals in ITRF2020
ITRF2020 periodic signals  CF frame
Annual & semiannual signals
available via https://itrf.ign.fr/en/solutions/ITRF2020

## Slide 4: Non-tidal loading models
ESMGFZ models (components NTAL, NTOL, HYDL, SLEL)  CF frame  time series analysis
Computed for all ITRF2020 GNSS stations
spatial resolution 0.5°, temporal 3h or 24h
available via isdc.gfz-potsdam.de/esmdata/loading/

## Slide 5: Comparison ITRF2020 - ESMGFZ
Difference ITRF2020 – ESMGFZ between the annual amplitudes
Red = ITRF2020 signal is larger, blue = ESMGFZ signal is larger

## Slide 6: Comparison ITRF2020 - ESMGFZ
Red = ITRF2020 signal is larger, blue = ESMGFZ signal is larger
Expectation: ITRF2020 signals are larger than ESMGFZ

## Slide 7: Comparison ITRF2020 - ESMGFZ
Red = ITRF2020 signal is larger, blue = ESMGFZ signal is larger
Expectation: ITRF2020 signals are larger than ESMGFZ

## Slide 8: Comparison ITRF2020 - ESMGFZ
WUHN
MAPA
Amazonas region, Brazil
Wuhan, China
Red = ITRF2020 signal is larger, blue = ESMGFZ signal is larger
Expectation: ITRF2020 signals are larger than ESMGFZ

## Slide 9: Introduction
Comparison of annual & semiannual amplitude and phase
Reduction of RMS (linear trajectory model), Reduction of periodic signals
Non-tidal loading models (ESMGFZ)
ITRF2020
GFZ repro3 solution
Periodic signals vs. NTL models
Correction at solution level (2000-2020)
Correction at observation level (2014-2015)
Periodic function:

## Slide 10: GFZ repro3 solution
Full reprocessing GPS / GLONASS / Galileo from 1994 to 2020
Satellite orbits and clocks, station coordinates, Earth rotation parameters
Products included troposphere delay and gradients, satellite attitude, biases
Statistics | 
Number of stations | 322
Number of satellites | 132 (G:67, R:39, E:26)
Number of daily solutions | 9962 (1994-2020) + extension for 2021-2022
Männel et al. (2021) https://doi.org/10.5880/GFZ.1.1.2021.001

## Slide 11: Corrections at solution level (GFZ repro3)

## Slide 12: Corrections at solution level (GFZ repro3)
Trajectory model including periodic (seasonal) functions (only stations > 1000 daily solutions):
Annual amplitudes in height decrease 3.20 ± 0.1  2.61 ± 0.1 mm
Semi-annual amplitudes are reduced (in height improvement for 85% of the stations)
diff. = corrected - uncorrected

## Slide 13: Corrections at solution level (GFZ repro3)
Trajectory model including periodic (seasonal) functions (only stations > 1000 daily solutions):
Semi-annual amplitudes in height decrease 0.96 ± 0.04  0.90 ± 0.03 mm
Semi-annual amplitudes are reduced (in height improvement for 90% of the stations)
diff. = corrected - uncorrected

## Slide 14: Corrections at solution level (GFZ repro3)
Linear trajectory model (2000-2020):
RMS reduction in North for 85%, in East for 73%, in height for 75% of the stations
Some stations show an increased RMS in the height coordinate (e.g., YELL, WUHN, YAKT …)
diff. = corrected - uncorrected

## Slide 15: Corrections at solution level (GFZ repro3)
WUHN
BRAZ

## Slide 16: Corrections at observation level (GFZ repro3)

## Slide 17: Corrections at observation level (GFZ repro3)
Linear trajectory model (2014-2015):
RMS reduction in North for 87%, in East for 76%, in height for 78% of the stations
Few stations show an increased RMS in the height coordinate (e.g., YELL, PARC, RIO2)
diff. = corrected - uncorrected

## Slide 18: Summary & Conclusion
Comparison of periodic signals in ITRF2020 and seasonal signals in non-tidal loading corrections (ESMGFZ models)
  Differences of annual amplitudes max. 10 mm
  mostly ITRF2020 > ESMGFZ, few stations with some interesting characteristics
Applying non-tidal loading corrections to GFZ repro3 coordinates (solution level)
   Reduction in annual and semi-annual signals (up to 5 mm) and coordinate RMS (up to 2.5 mm)
Applying non-tidal loading corrections at the observation level (preliminary 2014-2015)
   Reduction coordinate RMS (up to 2.5 mm)

## Slide 19
The impact of non-tidal surface loading deformation on GNSS coordinate time series
B. Männel1, S. Glaser1, A. Brandt1, and H. Schuh1,2
1 German Research Centre for Geosciences, Potsdam
2 Technische Universität Berlin

## Slide 20: Corrections at solution level
Trajectory model including periodic (seasonal) functions:
Annual amplitude
Semi-annual