## Slide 1
Zuheir Altamimi, Paul Rebischung, Xavier Collilieux, Laurent Métivier, Kristel Chanard
IGN-IPGP, France
ITRF2020: An overview of its features and results
Key Points:
ITRF2020 and its innovations: modelling of nonlinear station motions:
  Seasonal signals
  Post-Seismic Deformation for sites impacted by major earthquakes
Usage of ITRF2020 kinematic model
The story of the ITRF Scale

## Slide 2: ITRF2020 Input Data
TC | # of solutions | Time-span | # of sites | Theoretical Frame Origin
IDS/DORIS | 1456 weekly | 1993.0 – 2021.0 (28 yrs) | 87 | CM
IGS/GNSS/GPS | 9861 daily | 1994.0 – 2021.0 (27 yrs) | 1159 | CN
ILRS/SLR | 243 fortnightly 1460 weekly | 1983.0 – 1993.0 1993.0 – 2021.0 (38 yrs) | 100 | CM
IVS/VLBI | 6178 session-wise | 1980.0 – 2021.0 (41 yrs) | 117 | CN
IDS/DORIS
IGS/GNSS
ILRS/SLR
IVS/VLBI

## Slide 3: ITRF2020 Network
1223 sites
  878 Northern hemisphere
  355 Southern hemisphere
1800 stations
3106 discontinuities
~1159 GNSS sites
  1344 stations
  2938 discontinuities

## Slide 4
ITRF2020: Modelling nonlinear station motions
Red Stars: EQ Epicenters (65)
Green circles: ITRF2020 sites (118)
Impact of Periodic Signals
Impact of major earthquakes
Post-Seismic Deformation (PSD)
Refined PSD Parametric models:
Logarithmic Function
Exponential Function
Logarithmic + Exponential
Two Exponential Functions
Two Logarithmic Functions
Sine wave function

## Slide 5: ITRF2020 New Analysis Strategy
ITRF2020 Specifications:
Origin: SLR
Scale: Average of SLR & VLBI
Orientation: Alignment to ITRF2014
Data analysis:
Time series analysis & stacking of individual techniques
Assign discontinuities
Determine PSD Parametric Models using GNSS data
Estimate and remove the first 8 GPS draconitic harmonics
Accumulate the full 4 technique time series all together, adding local ties and co-motion constraints
Input data:
Space geodesy time series
  DORIS/IDS weekly
  GNSS/IGS daily
  SLR/ILRS weekly
  VLBI/IVS: Session-wise
Local ties: 253 vectors
Co-motion constraints at colocation sites:
  Station velocities & seasonal signals
Output:
Station positions & velocities
EOPs
PSD models
Seasonal Signals (annual & semi-annual) expressed in the CM of SLR

## Slide 6: ITRF2020: Augmented Parametric Reference Frame
Linear part
Post-Seismic Deformations (PSD)
Refined Parametric models
Seasonal Signals, expressed in the CM-SLR frame
ITRF2020 Kinematic Model:
Nonlinear part
See presentation by Xavier Collilieux, this afternoon

## Slide 7: Station seasonal signals, geocenter motion and the reference frame definition
CM : Center of Mass Frame
CF : Center of Figure Frame
(Blewitt, 2003)
Deformation
Xf : a & b are estimated in SLR CM-frame
(Geocenter motion)
See next presentation by Paul Rebischung

## Slide 8: Usage of ITRF2020 Seasonal Signals
The ITRF2020 kinematic model:
Precise Orbit Determination : Use CM-based seasonal signals
Alignment of global solutions: Use either CM or CF seasonal signals
==> (1) Avoid aliasing the seasonal signals into the Helmert parameters &
(2) Seasonal signals will accurately be retained in the aligned solutions
  If CM: translational motion common to all stations (i.e., seasonal geocenter motion) will be transferred to the aligned solutions
  If CF: the aligned solutions will be free from seasonal geocenter motion
Alignment of local or regional solutions: No seasonal signals to be used in order to avoid seasonal common mode in the aligned solutions

## Slide 9: The Story of the ITRF Scale: Scale of ITRF2020?
This is the first time of ITRF history where we have 4 independent and competitive scales stemming from the 4 techniques (DORIS, GNSS, SLR and VLBI)
IGS / GNSS scale is based on z-PCOs for Galileo Satellites, using 3.7 yrs of Galileo data
Improved ILRS / SLR scale determination with enhanced handling of range biases

## Slide 10: Preserving the intrinsic VLBI scale
Stack the time series, making use of the concept of Internal Constraints, a minimum-type of constraints (Altamimi et al., 2007), applied to the time series of any transformation parameter
For a given time series of a parameter (Pk), such as the scale, impose two conditions:

## Slide 11: IVS Intrinsic scale using all sessions in the scale definition

## Slide 12: IVS Intrinsic scale using selected sessions in the scale definition
Selected VLBI Sessions: Station networks with convex hull Volume ≥ 1019 m3

## Slide 13: IVS Intrinsic scale using selected sessions in the scale definition
Selected VLBI Sessions: Station networks with convex hull Volume ≥ 1019 m3
All sessions

## Slide 14: Scales with respect to ITRF2020
Orange: all VLBI Sessions
Red: Selected VLBI Sessions (convex hull volume ≥ 1019 m3 )
Light blue: all SLR time series
Dark blue: Selected SLR time series
Green: IGS/Repro3
Black: DORIS
Solution | Scale at 2015.0 (ppb) | Scale rate ppb/yr
IGS/GNSS | 0.682 ±0.018 | 0.018 ±0.001
IVS/VLBI | 0.075 ±0.040 | 0.000 ±0.003
ILRS/SLR | -0.075 ±0.038 | 0.000 ±0.004
IDS/DORIS | 1.386 ±0.037 | 0.028 ±0.003
Scale offset between SLR & VLBI is 0.15 ppb
(1 mm at the equator)
ITRF2020 scale: Average of red (VLBI) and dark blue (SLR)
mm

## Slide 15: Conclusion
ITRF2020
  A step further in improving the ITRF determination
  Adequately modelling nonlinear station motions
  Parametric models for PSD and seasonal signals
  Seasonal signals are provided in both CM SLR and CF frames
  ==> Seasonal geocenter motion
  We encourage the usage of Seasonal Signals in the processing of global solutions, including the GNSS/IGS daily and weekly solutions!
  For the first time in the ITRF history, the scale agreement between SLR & VLBI is at the level of 0.15 ppb (1 mm at the equator)
  Some nonlinearities in the scale time series still exist for SLR, VLBI and DORIS

## Slide 16: Thank you