## Slide 1: Deformation Models Progress with development of an OGC Standard
Richard Stanaway, Quickclose
Chris Crook, Land Information New Zealand
Kevin Kelly, ESRI
Roger Lott, IOGP
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022
Mw 7.8 earthquake, Kaikoura, New Zealand,
16th November 2016
Photo by Julian Thomson, GNS Science NZ

## Slide 2
Acknowledgements – IAG WG 1.3.1
Members
Richard Stanaway (Australia –WG Chair)
Wan Anom Wan Aris (Malaysia)
Elmar Brockmann (Switzerland)
Miltiadis Chatzinikos (Greece)
Yingyang Cheng (China)
Michael Craymer (Canada)
Chris Crook (New Zealand)
Nic Donnelly (New Zealand)
Kristian Evers (Denmark)
Jeff Freymueller (USA)
Pasi Häkli (Finland)
Muzaffer Kahveci (Turkey)
Kevin Kelly (USA)
Martin Lidberg (Sweden)
Roger Lott (UK)
Niraj Manandhar (Nepal)
Basara Miyahara (Japan)
José Antonio Tarrío Mosquera (Chile)
Chris Pearson (New Zealand)
Susilo (Indonesia)
Corresponding Members
Stylianos Bitharis (Greece)
Graeme Blick (New Zealand)
Carine Bruyninx (Belgium)
Xavier Collileux (France)
Paul Denys (New Zealand)
Patrick Forster (South Africa)
Mark Greaves (UK)
Leonid Lipatnikov (Russia)
Craig Roberts (Australia)
Hagi Ronen (Israel)
Yoshiyuki Tanaka (Japan)
Tatsuya Yamashita (Japan)
Norman Teferle (G.-D. Luxembourg
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 3
Motivation and purpose
Point-motion and time-dependent transformation models used in GNSS positioning need to match those used in GIS and spatial software to ensure consistent alignment over time accounting for geodynamics
“Non-geodetic” user expectation of “ground fixed” RF consistency over time
Consistent alignment of geodetic positioning and spatial data at any epoch
Map/data
(earlier epoch)
GNSS Position
(any epoch)
Map/data
(now)
displacement
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 4
The GIS problem with kinematic RF
GNSS Precise Point Positioning (PPP) is becoming ubiquitous and ~ 5 mm precision in a global reference frame is now routinely achievable (6+ hours static observations).
Coordinates of “ground fixed” points (survey control, cadastral boundaries, physical infrastructure, assets) are assumed to be stable or consistent in a local context over very long periods of time – This is a GIS user’s assumption.
But GNSS coordinates (natively in an ITRF aligned frame) of these “fixed” points change by up to several cm a year due to plate motion and by up to several metres during large earthquakes.
There has been no standardised approach to handle transformation between positioning and spatial data reference frames, especially in deforming zones.
The lack of a standard is a severe impediment to GIS , useable positioning precision and software development (with many agency specific approaches).
~2 m GIS “errors” due to lack of knowledge of kinematic RF are now very common!
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 5
Secular motion of ITRF PPP – Stable plate case
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022
ALIC – Alice Springs, Australia
Geoscience Australia
Nevada Geodetic Laboratory, UNR
ALIC – ATRF (Australian Terrestrial Reference Frame)

## Slide 6
ITRF PPP – plate boundary zone case
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022
Geonet, GNS Science, New Zealand
Mw 7.8 Kaikoura, New Zealand, 14th November 2016

## Slide 7
ITRF PPP – plate boundary zone case (contd.)
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022
SEDD, Seddon, New Zealand
Geonet, GNS Science, New Zealand
Land Information New Zealand

## Slide 8: Deformation models in applied geodesy
Geodetic agencies have used tightly integrated custom formats and software for managing crustal deformation effects
  Time-dependent transformations were not supported by GIS/coordinate transformation software
  No common format or structure for publishing of deformation models
In 2019 Land Information New Zealand (LINZ) commissioned the development of a deformation model transformation capability in PROJ based on a JSON “master file” referencing multiple GeoTIFF gridded data sets
OGC specification for standardising the description of deformation models with associated Geodetic Grid Exchange Format (GGXF). Collaboration with IAG WG 1.3.1 and bi-weekly web-meetings between June 2020 and early 2022 attended by many from IAG WG.
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 9: IAG/OGC – Deformation Model - agency survey (2020)
Responses from 27 countries on 5 continents
Mainly from geodetic/mapping agencies – potential producers of deformation models
9 have models in use, 10 in development, 4 planned
13 are velocity models, but 7 include some coseismic or postseismic models
Production systems mainly using custom formats and custom software. Recently some models implemented into PROJ coordinate system conversion library
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 10
Conformal transformation alone is not adequate
Current parametric conformal geodetic transformation strategies (e.g. 7 parameter, time-dependent 14/15-parameter and plate motion models PMM) are not suitable in deforming zones.
White regions are largely stable plate and a conformal time-dependent transformation approach is adequate for most applications
Coloured regions (plate boundaries and deforming zones) have high strain rates and a conventional parametric model is not adequate for NNR to crust-fixed RF transformations
From (Kreemer, C., Blewitt, G., and Klein, E. C. (2014), A geodetic plate motion and Global Strain Rate Model, Geochem. Geophys. Geosyst., 15, 3849– 3889, doi:10.1002/2014GC005407)
Overlain with ITRF2014 plate definition (Altamimi, A., Métivier, L., Rebischung, P., Rouby, H., Collilieux, X., ITRF2014 plate motion model, Geophysical Journal International, Volume 209, Issue 3, June 2017, Pages 1906–1912, https://doi.org/10.1093/gji/ggx136)
EURA
NOAM
NUBI
INDI
AUST
SOAM
ANTA
PCFC
PCFC
SOMA
ARAB
NAZC
GIA affected
regions
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 11
Conformal time-dep. transformation is only suitable in a stable plate interior
Australian continent is wholly within the stable portion of Australian Plate
(14 parameter / PMM adequate for parametric time-dependent transformation to a crust-fixed RF
Japan is almost completely within the plate boundary deforming zone, so a different approach is required
~ ITRF2014
Australian plate-motion model (PMM)
wx, wy, wz
No stable plate!
A simple parametric time-dependent (e.g. PMM derived) model is adequate for most applications
A gridded or triangulated (e.g. TIN) transformation model is more suitable to capture variability of the deformation field
From (Corné Kreemer, GSRM visualisation, UNAVCO
https://gsrm2.unavco.org/model/model.html )
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 12
time
position
Time-dependent reference frames
Kinematic (dynamic)
Earth-fixed NNR frame
Interseismic velocities are related to a time-invariant TRS and are usually non-zero – up to 90 mmyr-1
Kinematic (dynamic)
Plate-fixed reference frame
Interseismic velocities are near zero in stable portion of plate but increase near plate boundaries, GIA zones and other locally deforming areas
Semi-kinematic (semi-dynamic)
Crust-fixed reference frame
Interseismic velocity is implemented as zero – coordinates do not change during interseismic period however interseismic strain increases over time, requiring a frame reset when a strain tolerance limit is reached.
Interseismic motion
(e.g. ITRF2014 velocity)
Interseismic motion
(e.g. ETRF2014 velocity)
Interseismic motion
(implemented as 0
e.g. National
geodetic datum)
Coseismic
displacement
Postseismic
displacement
Typical point motion trajectories
In deforming zones
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 13
Velocity grid transformations – ITRF/IGS frame
(LINZ, 2021)
Velocity grid models are ideally suited to deforming zones and for GNSS-PPP to local (crust-fixed) reference frame transformations in lieu of a conformal parametric model. Single-step transformation process.
New Zealand
NZGD2000
Deformation
Model
Velocity grid
component
(ITRF96
horizontal
velocities)
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022
(Bitharis et al., 2016)
Hellenic
velocity
model
(ITRF2008)

## Slide 14
Velocity grid transformations – other ITRF/IGS examples
(Robin et al., 2020 – NRCan)
(Yamashita, GSI, 2021)
Canada Velocity Grid (CVG)
(IGS14 horizontal velocities)
Japan POS2JGD
(IGS14 horizontal
velocities)
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 15
Plate-fixed velocities are typically close to zero within the stable plate interior but become non-zero near plate boundaries or GIA regions. Transformation from ITRF/IGS to plate-fixed RF at different epochs becomes a two step process
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022
European velocity grid (in Eurasian frame)
Elmar Brockmann, swisstopo, 2022
http://pnac.swisstopo.admin.ch/divers/dens_vel/000.html
Velocity grid transformations – Plate fixed RF

## Slide 16
Coseismic displacements
There is an expectation that coordinates of “ground fixed” reference frames will change after an earthquake. Especially considering surface fault ruptures and relative coordinate strain. Expectation is less clear in the far field.
A coseismic displacement model is required for each significant displacement event to enable transformation of coordinates across different seismic epochs
Examples:
Transformation of post-earthquake PPP position to a pre-earthquake frame
Transformation of cadastral or engineering designs in a pre-earthquake frame to a post-earthquake reference frame
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 17
Coseismic displacement model
NZGD2000v20000101
NZGD2000v20130801
NZGD2000v20180701
Coseismic displacement model for 2010 and 2011 Christchurch earthquake sequence (and others)
Coseismic displacement model for 2016 Kaikoura earthquake and others.
(yyyymmdd)
Transformation between each “version” is a step function using interpolation of a nested coseismic displacement grid (patch).
Higher order nesting can be used near surface fault scarps in lieu of a triangulated model.
Christchurch, New Zealand. (Crook et al., 2016)
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 18
Postseismic and slow-slip events (SSE)
Working approximation using a piecewise or step function
Optimal approach using composite logarithmic and exponential function
SSE can be modelled as a piecewise function (interseismic + SSE velocity), hyperbolic tangent function or smoothed as an averaged linear velocity if the SSE displacement is within a positioning tolerance threshold.
(Gisborne (GISB) New Zealand, East time-series showing Slow Slip Events, GNS, 2018 and Stanaway, 2020)
(Seddon (SEDD) New Zealand, East time-series showing postseismic displacement after Kaikoura earthquake sequence, November 2016,, GNS, 2018 and Stanaway, 2020)
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 19
time
position
Interframe transformation logic flow
t0 =2000.0
t2
t1
t2
t2
t1
Separate interseismic velocity and coseismic displacement models are useful
Intraframe version transformation
from NZGD2000v20180701 to NZGD2000v20000101 using coseismic displacement model (subtracted)
(e.g. to align position at t2 with legacy spatial data defined in a pre-earthquake frame at t1 )
Kinematic RF
(e.g. ITRF96)
Crust-fixed RF
(e.g. NZGD2000)
NZGD2000v20000101
NZGD2000v20180701
Intraframe propagation
from t2 to t0 using velocity model
(ITRF96 as used in NZ)
This aligns closely with the latest version of NZGD2000 (NZGD2000v20180701)
(ITRFyyyy to ITRF96 transformation also required at t2 if
position is observed in a later realisation of ITRF)
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 20: High level structure of deformation model
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 21: Timeline
GGXF (Geodetic gridded data exchange format) and deformation model functional model teams established in June 2020
GGXF project to determine a common format for geodetic data sets
Deformation model to determine a common structure for defining deformation models for use in coordinate time-dependent transformation operations
Teams have been meeting on alternate fortnights – meetings well supported
Deformation model team working in conjunction with IAG (International Association of Geodesy) WG 1.3.1 on "Time-dependent transformations between reference frames in deforming regions".
Deformation models are structurally more complex than other gridded geodetic data sets - has dictated scope of GGXF, and depends on GGXF for realization
Project artefacts in https://github.com/opengeospatial/CRS-Deformation-Models
16th June 2022 - Abstract Specification presented at 123rd OGC Member Meeting in Madrid
August 2022 – progressed to OGC Standards Working Group (SWG)
ISO Standard development (largely based on OGC Standard) 2023?
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 22: Abstract specification exclusions
Does not support other representations of deformation such as:
  Triangulated spatial models (e.g. TINs)
  rigid body transformations between reference frames such as time dependent Helmert or Bursa-Wolf transformations (e.g. 14/15 par.),
  trajectory models for individual stations, such as those described for ITRF geodetic monuments
  Plate motion models (PMMs),
  three dimensional geophysical models of deformation in terms of dislocations on fault planes such as elastic half space (Okada) or finite element models.
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 23: Geodetic Grid Exchange Format (GGXF)
Abstract specification of GGXF structure
YAML text based format
Proof of concept YAML/NetCDF implementation
NetCDF agreed binary carrier
NetCDF implementation choices:
  Investigating alignment with CF conventions
  Investigating ACDD NetCDF metadata conventions
  NetCDF structure decided
Next steps:
Documentation of NetCDF profile
Update NetCDF proof of concept Github implementation and example data sets
https://github.com/opengeospatial/CRS-Gridded-Geodetic-data-eXchange-Format
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022

## Slide 24
https://github.com/opengeospatial/CRS-Deformation-Models/blob/master/products/specification/abstract-specification-deformation-model-functional-model.pdf
IAG Commission 1, REFAG 2022, Thessaloniki, Greece, 17-20 October 2022
Ευχαριστώ!